## Slide 1
Chapter 2
Complex Network Reliability Evaluation and Estimation in cyber-risk
Cyber-Risk Informatics: Engineering Evaluation with Data Science

## Slide 2: Learning Objectives
This chapter describes a scalable innovative “overlap technique” to tackle large complex networks’ reliability evaluation difficulties, which cannot be handled by straightforward RBD (reliability block diagramming) techniques used for the simple parallel-series topologies.
Reliability analysis is the process of quantifying an embedded system’s ingress (s=source) to egress (t=target) or ‘s-t’ serviceability by examining the dependency relationships between the components.
Monte Carlo simulations demonstrate the methods discussed. A) Static (time-independent), B) Dynamic (time-dependent), and C) Multi-state versions to include derated behavior, beyond conventionally up and down states, are illustrated for calculating the directional s-t reliability of complex networks.

## Slide 3: Abstract
This chapter beyond presenting a spectrum of network reliability methods studied in the past decades, describes a scalable innovative “overlap technique” to tackle large complex networks’ reliability evaluation difficulties, which cannot be handled by straightforward RBD (reliability block diagramming) techniques used for the simple parallel-series topologies. Reliability analysis is the process of quantifying an embedded system’s ingress (s=source) to egress (t=target) or ‘s-t’ serviceability by examining the dependency relationships between the components. Every embedded system, whether simple or complex, can be decomposed into components (blocks) and transmissions (links) within a topology. A large amount of work is in progress on reliability block diagramming techniques. Another body of dynamic research is in digital testing of embedded systems with VLSI (very large scale integrated) circuits. Examples are shown on how to apply the Overlap Algorithm to compute the ingress-egress reliability. Monte Carlo simulations verify these methods. Namely, A) Static (time-independent) or constant, B) Dynamic (time-dependent) with Weibull distribution to represent the multiple stages of components from infancy to useful-life period and to wear-out, and C) Multi-state versions to include derated behavior, beyond conventionally up and down states, are illustrated for calculating the directional s-t reliability of complex networks.
Keywords: Reliability, RBD, s-t (source-target), component, network, overlap, pdf, cdf, UP, complex, static, multi-state, dynamic, Weibull, ERBDC, LSE, DOWN, DER.

## Slide 4: INTRODUCTION AND MOTIVATION
Network reliability is the probability that a network with all its sub-networks and constituting components will successfully complete the task it is intended to perform under the conditions encountered for the specified period of time defined between a source and a target.
Network reliability computations are similar to those developed for industrial applications, but there are a few exceptions. In industrial applications, all of the components in the system are usually considered critical to the overall function of the system. However, in network applications, the target communication between two nodes may select few components in the system due to redundancy.
Network reliability estimation has been used successfully for non-trivial-sized networks using neural networks and heuristic algorithms as well as employing a concurrent error detection approach by the co-author of an earlier research.

## Slide 5: Overlap Technique to Calculate Complex Network Reliability
Network State Enumeration and Example 1:
Consider the 5 node sample network in Figure beside.
Each node has a reliability of 0.9, meaning that 90% of the time it is up (operating, functional, working, etc.) while 10% of the time it is down (not operating, dysfunctional, not working, etc).
The state diagram would look like the following. The “1-5 Probability” column is only populated in 25 = 32 states that constitute a complete link between node 1 and node 5, where the rest are left out with zero results in below slide Table.

## Slide 6: Overlap Technique to Calculate Complex Network Reliability (cont’d)
Five node/two path static network state enumeration table for “1-5” in above slide Figure:
Note that this returns the same results as standard parallel-series equations that can be done manually:
RT = R1 × (1 – ((1 - R3) × (1 – R2 × R4))) × R5
RT = 0.9 × (1 – ((1 – 0.9) × (1 – 0.9 × 0.9))) × 0.9 = 0.79461

## Slide 7: Overlap Technique to Calculate Complex Network Reliability (cont’d)
Consider the same 5 node network, we can quickly deduce that the two unique paths through the system from node 1 to node 5 are {1→3→5} and {1→2→4→5}.
More on algorithmically determining paths will follow. If all of the nodes in either path are up, there will be a continuous connection between the source and target nodes. If we map the two paths in the state diagram below (all of the states where node 1 is down have been hidden to reduce the size), we find that the sum of two reliabilities (=1.385) is exactly 0.59049 greater than the desired result.
This is the probability of overlap between the two paths. The overlap is found by taking a union of all the nodes in both paths. This union is simply a mathematical state overlap and does not need to represent a path across.

## Slide 8: Overlap Technique to Calculate Complex Network Reliability (cont’d)
Five node/two path static network state table with useful paths for “1-5” Figure
Unfortunately, reliability calculation for complex networks is not as simple as subtracting the overlaps between unique paths.
When there are more than two paths, many states may overlap across multiple paths. When subtracting overlaps any state that has been subtracted more than once will have to be re-added to the final result.

## Slide 9: Overlap Technique to Calculate Complex Network Reliability (cont’d)
Generating Minimal Paths and Example 2:
This practice into the binary nature of reliability networks and the overlapping characteristics of path reliabilities lends itself to the idea of a structured algorithm that could compute a finite set of minimal paths from ingress to egress, one considers the individual reliabilities of each path, and programmatically adjusts for overlaps.
The first step, determining a set of minimal paths, is of utmost importance regarding efficiency and scalability.
The order of the nodes is not important as the set of minimal paths generated will be the same regardless of order. Start by pushing the start node onto the initially empty stack and repeat the following algorithm on the top stack node until the stack is again empty.

## Slide 10
1. If the top node connects directly to the target node: Push the target node onto the stack.
  a. Save the current stack as a new minimal path (the bottom node is the start node and represents the start of the minimal path while the top node is now the target node representing the end of the path).
  b. Pop the top two nodes (the target node and the node that links directly to it) off of the stack.
2. If the top node does not connect directly to the target node, push the next connecting node onto the stack. The next connecting node can be determined by the following logic:
  a. No node that is already in the stack is a candidate. This would cause a recursion issue as paths could fall into a recurring loop that grows infinitely in size without ever reaching the target node.
  b. If the previous action was a push action (i.e. the current node was newly pushed onto the stack) choose the lowest ordered node connected to the top stack node that is not already in the stack.
  c. If the previous action was a pop action (i.e. one of the nodes connected to the top node had finished its iterations and was removed) choose the next ordered node connected to the top stack node after the previously popped node.
3. If the top node does not connect directly to the target node and no new connecting node was found to push onto the stack, pop the top node off the stack.

## Slide 11: Overlap Technique to Calculate Complex Network Reliability (cont’d)
Using the simple network depicted in below figure, it is possible to walk through the minimal path algorithm step by step (following slides) to find the set of minimal paths across the network starting from node 1 and traversing to node 6.

## Slide 12
Step 1: Add the start node to the stack:
Step 2: The top node (1) connect to both nodes 2 and 3 and neither one is already in the stack. As the last action was a push action, push the lowest order node, 2, to the stack.
Step 3: The top node (2) connects to nodes 1 and 4, but 1 is already in the stack, so push node 4 onto the stack.
Step 4: Because the top node (4) links directly to the target node (6), push 6 onto the stack and save the current stack as a minimal path. Then, pop the top two nodes off of the stack. Note: even though there are still possible paths through node 4 (e.g. 1, 2, 4, 3, 5, 6), any such path will be short circuited by 1,2,4,6 and thus will not need to be considered as a minimal path. Therefore, node 4 can be popped from the stack.
1
1
2

## Slide 13
Step 5: Because node 4 was just popped from the stack and the top node on the stack (2) does not link to any nodes higher than 4, pop node 2 off the stack.
Step 6: Node 2 was just popped off the stack; the next higher node than 2 connected to the top stack node (1) that is not already in the stack is node 3. Push node 3 onto the stack.
Step 7: The top node (3) connects to nodes 1, 4, and 5, but 1 is already in the stack, so push the lowest (4) remaining node onto the stack.
Step 8: The top node (4) connects directly to the target node (6), push 6 on the stack and save the current stack as a minimal path. Then, pop the top two nodes off the stack. Note: At this point, it is clear to see that if node 4 did not link directly to the target node, node 2 would have been the first node to be pushed onto the stack. But, from node 2 there would be no way to link to the target node (6) without passing through any nodes already in the stack. In this case, the process would still need to consider node 2 to insure total algorithm inclusion. In small networks such as this example, it is easy to visualize dead-ends, but in a very large network, they may not be so clear and taking shortcuts could result in missed paths and thus incorrect results.

## Slide 14
Step 9: Because node 4 was just popped off the stack, the next highest node connected to the top node (3) that is not already in the stack is node 5. Push node 5 on to the stack.
Step 10: The top node (5) connects directly to the target node (6), push 6 on the stack and save the current stack as a minimal path. Then, pop the top two nodes off the stack.

## Slide 15
Step 11: Node 5 was just popped off the stack and there are no higher nodes connected to the top node (3), pop node 3 off of the stack.
Step 12: Node 3 was just popped off the stack and there are no higher nodes connected to the top node (1), pop node 1 off of the stack.
Step 13: The stack is now empty; the algorithm is complete. The minimum paths generated above are as follows:
The core algorithms presented here never consider link reliabilities. When link reliabilities are required, think of each link as a node itself.

## Slide 16
When link reliabilities are required, think of each link as a node itself. Of interesting note is, when considering link reliabilities, steps that would have resulted in an immediate link to the target node (i.e. steps 4, 8, and 10 in the minimal paths example), now have opportunities to venture down additional paths. Networks with link reliability tend to have several more minimal paths than their counterparts without link reliabilities. See Example 2’s Figure as follows:

## Slide 17
Overlap Method Algorithmic Rules and Example 3:

## Slide 18
To continue with Example 3 for the complex network in Figure below, if all the nodes are 0.9; using “overlap” algorithm:
IN-OUT {7-8} = {7} [ {1-4} + {1-5} + {2-5} + {3-5} + {3-6} – {1-4-5} – {1-2-5} – {1-2-4-6} – {2-5-6}–{1-3-4-6} –{1-3-5-6}–{2-3-6}+{1-2-4-5-6}+{1-2-3-4-6} –{1-2-3-4-5-6}]{8}
IN-OUT {7-8} = (0.9) {(5) (0.92) – [(4) (0.93) + (3) (0.94)] + (4) (0.95) – (0.96)} (0.9)
= (0.9) { (5)(0.81) – (4)(0.729) – 3 (0.6561) + 4 (0.59049) – 0.531441} (0.9)
= (0.9) {4.05 – 4.8843 + 2.36196 – 0.531441} (0.9) = (0.996219) (0.81) = 0.80694

## Slide 19
Overlap Method Algorithmic Rules and Example 3:

## Slide 20: The Overlap Method: Monte Carlo and Discrete-Event Simulation
For time-dependent discrete event simulation technique, assume the rates for each component, such as = (mean sojourn time) –1.
Let us assume that the probability of “up” for a component, such as 0.9 denotes 9 time units out of 10 are operating, and 1 time unit out of 10 not operating. The reciprocals of the means yield the rates: (failure rate) = 1/9, and (repair rate) =1/1. Thus, FOR (Forced Outage Rate or Unavailability) = / ( + ) = (1/9) / [(1/9) + (1/1)] = (1/9) / (10/9) = 0.1.
Using these rates of sojourn to generate times to failure with a negative exponential pdf, one travels from component to component. If both sending and receiving ends operate at the same time, it is a successful connection. How many successes out of how many “n” trials, such as from s = 1 to t = 19 as in the Figure on the next slide, is the solution.

## Slide 22
19-node (s=1, t=19) complex network with Monte Carlo simulation (83 seconds) and analytical results (50 seconds), both 0.784 with simulation taking 33 more seconds.

## Slide 23
Example 5’s simulation for (s=1, t=52) with 72 links is 0.558 in 17119 seconds, and the faster analytical result is 0.556 in 18.034 seconds in 0.1% of the simulation time. More simulation runs, the closer results will converge as in the Figure on the next slide.

## Slide 25: MULTISTATE SYSTEM RELIABILITY EVALUATION (cont’d)
Simple Series System with Single Derated States:
A simple series system with fully operating and derated states is shown in below Figure of Example 6:

## Slide 26: MULTISTATE SYSTEM RELIABILITY EVALUATION (cont’d)
Our goal is to calculate the simplest series system reliability of a primitive example, where the node has three states, with probabilities, P (UP) = 0.7, P (DER) = 0.2 and P (DN) = 0.1 in Figure above.
We use two approaches. In this example, there can be SN = 32 = 9 combinations, where S is the number of states and N is the number of nodes. S = 3 and N = 2; this is the long way. Working on the same two-node simple series system, let’s calculate the system up, derated and down probabilities in Figure above in a shorter way.
Psys (UP) = P1 (UP) P2 (UP) = (0.7) (0.7) = 0.49
Psys (DER) = P1 (UP+DER) P2 (UP+DER) – Psys (UP) = (0.7 + 0.2)2 – 0.72 = 0.81 – 0.49
= 0.32
Psys(DN) = 1 – Psys(UP) – Psys(DER) = 1 – 0.49 – 0.32 = 0.19

## Slide 27: MULTISTATE SYSTEM RELIABILITY EVALUATION (cont’d)
Active Parallel System:
The system with IN (1) and OUT (4) both perfect, 2 and 3 DER are shown in Figure below of Example 7.

## Slide 28: MULTISTATE SYSTEM RELIABILITY EVALUATION (cont’d)
Working on the same four-node simple parallel-series system, let’s calculate the system up, derated and down probabilities in the Figure in the previous slide with a shortcut formulation approach.
Psys (UP) = P1 (UP) {1 – [1– P2 (UP)] [1– P3 (UP)] } P4 (UP)
= (1.0) [1 – (1 – 0.7)2] (1.0) = (1.0) (0.91) = 0.91
Psys (DER) = P1 (UP) P4 (UP) – [1– {1 – P2 (UP+DER)} {1– P3 (UP+DER)} ] – Psys
(UP) = 1 * (1– 0.12) – 0.91 = 0.99 – 0.91 = 0.08
Psys(DN) = 1– Psys(UP) – Psys(DER) = 1– 0.91– 0.08 = 0.01

## Slide 29
Simple Series-Parallel System:
A simple parallel-series system with derated states is shown in Figure below in Example 8.
MULTISTATE SYSTEM RELIABILITY EVALUATION (CONT’D)

## Slide 30: MULTISTATE SYSTEM RELIABILITY EVALUATION (CONT’D)
The parallel and series topologies merged will contain 34 = 81 combinations, such as UP-UP-UP-UP, DER-UP-UP-UP all the way to DN-DN-DN-DN.
This method is cumbersome and time consuming to distinguish the desirable states by enumerating. The shortcut technique is faster as follows.
P (UP) = P1 (UP) P4 (UP) {1– [1– P2 (UP)][1– P2 (UP)]} = (0.7) (0.7) [1– (1 – 0.7)2] = (0.49) (0.91) = 0.4459
Psys (DER) = P1 (UP+DER) P4 (UP+DER) – {1– [1– P2 (UP)] [1– P3 (UP)]} – Psys (UP) = (0.7+0.2)2(1– 0.12) – 0.4459 = (0.81) (0.99) – 0.4459 = 0.356
Psys(DN) = 1 – Psys(UP) – Psys(DER) = 1 – 0.4459 – 0.356 = 0.19

## Slide 31: MULTISTATE SYSTEM RELIABILITY EVALUATION (CONT’D)
A Simple Series-Parallel System with Multistate Components:
A simple parallel-series system with derated and degrades states is shown in Figure below in Example 9.

## Slide 32: MULTISTATE SYSTEM RELIABILITY EVALUATION (CONT’D)
Using the short-cut formulation approach (the state-enumeration method requires SN = 44 = 256 combinations in general; here, due to 1 and 4 being full states, 42 = 16, and therefore cumbersome to work with), we get, using the same logic as we used earlier.
P (UP) = P1 (UP) P4 (UP) {1– [1– P2 (UP)] [1– P3 (UP)] } = (1.0) [1– (1 – 0.4)2] = 1 – 0.36 = 0.64
Psys (DER) = (1.0) {1– [1– P2 (UP+DER)] [1– P3 (UP+DER)] } – Psys (UP) = (1.0) (1– 0.32) – 0.64 = 0.91 – 0.64 = 0.27
Psys(DEGR) = (1.0) * {1– [1– P2 (UP+DER+DEGR)] [1– P3 (UP+DER+DEGR)] } – Psys(UP) – Psys(DER) = (1.0) (1 – .12) – 0.64 – 0.27 = 0.99 – 0.64 – 0.27 = 0.08
Psys(DN) = 1– Psys(UP) – Psys(DER) – Psys(DEGR) = 1 – 0.64 – 0.27 – 0.08 = 0.01

## Slide 33: MULTISTATE SYSTEM RELIABILITY EVALUATION (CONT’D)
A Combined System: Power-Plant Example:
A hydroelectric power plant in Figure 10 can generate 100 % (fully operating), 75% (derated 1), 50% (derated 2), 25% (derated 3) or 0% (fully down) of rated electric power capacity depending on the water storage level and thus the amount of steam flow reaching the turbine.
The corresponding system states are 1, 2, 3, 4, and 5. The power plant consists of four turbines in active parallel and an output transformer in series with the turbines.
The available turbine with maximal power is used.

## Slide 34: MULTISTATE SYSTEM RELIABILITY EVALUATION (CONT’D)
A Combined System: Power-Plant Example:
For any demand level of w = 1, 2, 3, 4, 5, the combined system reliability of states takes the recursive form in Example 10:
where, w=1, 2, 3, 4, 5 and Rsys (0) = 0.0.

## Slide 35: MULTISTATE SYSTEM RELIABILITY EVALUATION (CONT’D)
MSS (Multistate system) elements are statistically independent.
If Rw1 = 0.4, Rw2 = 0.3, Rw3 = 0.15, Rw4 = 0.1 and Rw5 = 0.05, w (state) = 1… 5 as shown in Figure below; then the system reliabilities Rsys (w) are:
Rsys (1) = 0.4[1– (1 – 0.4)4] = 0.34816
Rsys (2) = (0.4 + 0.3) {1 – [1 – (0.4 + 0.3)] 4} – R (1) = 0.69433 – 0.34816 = 0.34617
Rsys (3) = (0.4 + 0.3 + 0.15) {1–[1–(0.4 + 0.3 + 0.15)] 4} – R (1)–R (2) = 0.15524
Rsys (4) = (0.4 + 0.3 + 0.15 + 0.1) {1– [1 – (0.4 + 0.3 + 0.15 + 0.1)] 4} –R (1) –R (2) –R (3) = 0.10042
Rsys (5) = (0.4 + 0.3 + 0.15 + 0.1 + 0.05) {1– [1 – (0.4 + 0.3 + 0.15 + 0.1 + 0.05)] 4} –
R (1) – R (2)–R (3) – R (4) =1– R (1) – R (2) – R (3) – R (4) = 1 – 0.10042 – 0.15524 – 0.34617 –0.34816 =0.05001

## Slide 36: MULTISTATE SYSTEM RELIABILITY EVALUATION (CONT’D)
Example 10’s Power Plant with four derated turbines (nodes 1 to 4) in parallel and a transformer (egress node 5) in series, and node 0 (as an ingress node with full reliability).

## Slide 37: MULTISTATE SYSTEM RELIABILITY EVALUATION (CONT’D)
Large Network Examples Using Multistate Overlap Technique:
For the 19-Node large cyber network, we can calculate the ingress-egress overlap reliability using multi-state (up=0.7, derated=0.2, down=0.1) as shown in Figure 11 for Example 11:

## Slide 38: Example 12’s Implementation of Multi-State overlap reliability to 52-node network in 18s. Solution 1-52: Full Reliability=0.05, Derated Reliability= 0.51, Full Unreliability= 0.44.

## Slide 39: Weibull Time-Distributed Reliability Evaluation
Motivation behind Weibull Probability Modeling:
The benefit of choosing Weibull distribution is that we can implement the generic mathematical behavior once and satisfy a wide range of component behavior by simply manipulating the shape parameter, β, at runtime. As shown in the subsequent graph of Figure below, the entirety of component behavior is spanned.

## Slide 40: Weibull Time-Distributed Reliability Evaluation (Cont’d)
Weibull Parameter Estimation Methodology:
Inside the overlap algorithm, there are three types of arithmetic performed on node reliabilities; multiplication, addition, and subtraction. In order to incorporate Weibull reliability directly into the algorithm, we must first find a way to define and implement Weibull math.
Consider the fact that at t=0 a two-parameter Weibull reliability should always be 1; if we were to add two components the value of t=0 would be 1+1 or 2, directly conflicting with the reliability bounds.. The solution lies in breaking the reliability of each component into an array of static reliabilities at evenly distributed points in time. The overlap algorithm is run generating a multitude of reliabilities. Finally, the reliability plot is used to generate a final Weibull goodness of fit.

## Slide 41: Weibull Time-Distributed Reliability Evaluation (Cont’d)
Overlap Algorithm Applied to Weibull Distributed Components:

## Slide 42: Weibull Time-Distributed Reliability Evaluation (Cont’d)
Overlap Algorithm Applied to Weibull Distributed Components:
Before delving into how to estimate a final pair of shape and scale parameters from the solution generated by the overlap algorithm, let’s first walk through an example of a slightly more complex network up to this point.
Consider the following network figure from node 1 to node 19 in which each node has both β and α equal to 1 assumed.
See Example 13’s nineteen-node Weibull network in Table above and Figure below.

## Slide 44: Weibull Time-Distributed Reliability Evaluation (Cont’d)
Estimating Weibull Parameters:
Graphing the above equation depicts an exponential curve with a power of β (=slope) in the figure below.

## Slide 45: Weibull Time-Distributed Reliability Evaluation (Cont’d)
Estimating Weibull Parameters:
To determine the value of β, take the log of both axis and use linear least squares to determine the slope. See the figure below.

## Slide 46: Weibull Time-Distributed Reliability Evaluation (Cont’d)
Estimating Weibull Parameters:
The x-coordinates are given by log (t) while the y-coordinates are log (-ln(r)).
The best line’s slope function for calculating first-degree polynomials for n number of x and y plot points are given for the standard slope formula “m” for the Weibull slope, “β” respectively, as follows:

## Slide 47: Weibull Time-Distributed Reliability Evaluation (Cont’d)
Estimating Weibull Parameters:
Substituting the x and y plot functions from above yields the slope to attain the LSE (Least Square Estimation):
Extrapolate the values in the plot table to quickly find the various sums.
The number of plot points, n, is 30. The first and last points are omitted as the values of 0 for time and reliability would cause the log functions to return -∞. Solve for β and α below respectively:

## Slide 48: Weibull Time-Distributed Reliability Evaluation (Cont’d)
Estimating Weibull Parameters:
Substituting the x and y plot functions from above yields the slope to attain the LSE (Least Square Estimation):
Extrapolate the values in the plot table to quickly find the various sums. The number of plot points, n, is 30. The first and last points are omitted as the values of 0 for time and reliability would cause the log functions to return -∞. Solve for β and α below respectively: β = 1.16

## Slide 49: Weibull Time-Distributed Reliability Evaluation (Cont’d)
Estimating Weibull Parameters:
Use the value of β to estimate for α. Recall the modified exponential equation
-ln(r) 1/β = t / α
Solving for α generates:
α = t / -ln(r) 1/β
α = t / -ln(r) 1/1.159524
α = t / -ln(r) 0.862423
Graphing t vs. -ln(r) 0.862423 produces a regression line, the slope of which is 1/α. Again, we use the linear least squares estimation (LSE) principle to approximate the value for α. As the slope of the line is the inverse of the scale parameter, the inverse of the least squares slope formula is used for result interpretation.

## Slide 50: Weibull Time-Distributed Reliability Evaluation (Cont’d)
Estimating Weibull Parameters:
Use the equation obtained above to solve for α:
α = 0.354085

## Slide 51: Weibull Time-Distributed Reliability Evaluation (Cont’d)
Estimating Weibull Parameters:
Linear graph for 1/α.

## Slide 52: Weibull Time-Distributed Reliability Evaluation (Cont’d)
Estimating Weibull Parameters:
Nineteen-node (See Slide 42) Weibull results for graphical comparison.

## Slide 53: Weibull Time-Distributed Reliability Evaluation (Cont’d)
Fifty-two Node Weibull Example for Estimating Weibull Parameters:

## Slide 54: Weibull Time-Distributed Reliability Evaluation (Cont’d)
Fifty-two Node Weibull Example for Estimating Weibull Parameters:
Note that the more points, the more accurate the plot will be; but more microprocessor run-time will be observed.
Find the sums of each of the calculated columns and apply the values to the equation for the shape parameter.
Given the new-found value for β compute the values required to estimate the scale parameter α. Calculate -ln( r )1/β, t2 and t(-ln( r )1/β )and their corresponding sums across the plot.
, = =1.370000185

## Slide 55: Weibull Time-Distributed Reliability Evaluation (Cont’d)
A Weibull Network Example from an Oil Rig:
Given Figure below diagram, with the physical shape and contour [ ]; the network reliability (s=1, t=8) is calculated to be 77.2 %.
All components have 0.9 reliability including the ground at 9.

## Slide 56: Simple onshore land-based oil rig structure with input-output contour diagram. A Weibull Network Example from an Oil Rig (Cont’d):

## Slide 57: . A Weibull Network Example from an Oil Rig (Cont’d): The benefits listed above prove that we have documented an algorithm with a true industry application, while the shortcomings really only detail opportunities for growth rather than steadfast barriers

## Slide 58: Discussions and Conclusion
The network reliability evaluation algorithm may open many doors in the vast reliability engineering field. The overlap algorithm presented in this chapter, along with the associated performance tuning activities, greatly increases the size and complexity of the networks that are possible.
This expansion of capability moves the presented set of algorithms from a tool that can only be used in demonstrations and educational activities to an enterprise level solution than can be used to capably solve real-world scenarios as illustrated in the next two slides.
In applications such as monitoring a packet-switching network, professionals can plan for situations where traffic controlling hubs may experience heavy systems loads and operated in a derated state.

## Slide 59: THANK YOU!