## Slide 1
Chapter 4
Security Risk Assessment and Management in cyber-risk
Cyber-Risk Informatics: Engineering Evaluation with Data Science

## Slide 2: LEARNING OBJECTIVES
Quantitative risk measurements are absolutely needed to compare design alternatives and calculate monetary outcomes for mitigating risk.
Along with the purely quantitative security meter model as the data allows, we consider a security meter model for qualitative attributes.
Security meter (SM) design provides the conveniences of risk measurements in a quantitative manner that is much required in the security world
The model proposed is practical and simple to use for beginners in the field, but it also provides a mathematical–statistical foundation for risk valuation.
Further, the triple product rule math-statistically will theoretically verify the SM machinery. Last but not least, game-theoretic risk optimization and mitigation will be shown for multi-theme practices.

## Slide 3: Abstract
Quantitative risk measurements are absolutely needed to compare design alternatives and calculate monetary outcomes for mitigating risk. There are very few if any, quantitative measures in academia or corporate world, other than high, medium, or low classifications. Along with the purely quantitative security meter model as the data allow, we consider a security meter model for qualitative attributes. Following, prioritization of software maintenance is also achieved by ranking the vulnerabilities through a Bayesian analysis. Further, the imperfections such as the nondisjointness of the vulnerabilities and the threats are treated using laws of probability. The model proposed is practical and simple to use for beginners in the field, but it also provides a mathematical–statistical foundation for risk valuation. The probabilistic assumptions for the Monte Carlo simulation revolve around using a simple uniformly distributed random variable for the input variables by assigning an upper and a lower bound. Further, the triple product rule math will theoretically verify the SM machinery. Last but not least, game-theoretic risk optimization and mitigation will be implemented to certain multi-theme practices selected. These models will be supported by a fine-tuned practical software package, CyberRiskSolver for computational ease and time-saving convenience to learn faster.
Keywords: Risk, vulnerability, threat, countermeasure, security meter, quantitative, qualitative, hybrid, management, cost-effective, Bayesian, simulation

## Slide 4: INTRODUCTION
There are virtually no such quantitative and probabilistic measures in the academia or corporate circles other than high, medium or low denominations which are descriptive, subjective and free to any interpretations as one pleases. They do not carry analytical monetary evaluations for comparisons when mitigation is done.
Among those existing analyses that favor a quantitative study, either i) there is no probabilistic frame about whether to add or multiply risks in a correct probabilistic frame of mind, ii) the risk calculations are handled on singular basis without a system.
In pursuit of a practical and accurate statistical design, security breaches will be recorded, and then the model’s input probabilities will be estimated using the equations that were developed.
Undesirable threats that take advantage of hardware and software weaknesses or vulnerabilities can impact the violation and breakdown of availability (readiness for usage), integrity (accuracy), conﬁdentiality (provision of secrecy), and nonrepudiation (inability to deny), as well as other aspects of software security such as authentication (evidence of identity), privacy (provision of personal information), and encryption (ability to code/decode using a key).

## Slide 5: What Other Scoring Methods are Available?
Other qualitative models and methods, such as Attack Trees, and Time-to-Defeat are only deterministic but not quantitative or cost-convertible. Recently, various scoring systems have mushroomed on the internet such as CVSS, NVD and others, as follows and illustrated on subsequent slides.
Common Vulnerability Scoring System (CVSS): This is a free and open industry standard for assessing the severity of computer system security vulnerabilities.
National Vulnerability Database Version 2.2 (NVD): This is the U.S. government repository of standards-based vulnerability management data presented using the Security Content Automation Protocol (SCAP). This data enables automation of vulnerability management, security measurement, and compliance. NVD includes databases of security checklists, security related software flaws, misconfigurations, product names, and impact metrics. In particular, NVD supports the Common Vulnerability Scoring System (CVSS) version 2 standards for all CVE vulnerabilities.
JVNRSS: CVSS Version 2.0 (JVN): JVN provides the "Vendor Status Notes (VN)" and the "Status Tracking Notes (TRnotes)". VN is a service providing information on how to fix vulnerabilities. It is similar to the "CERT Vulnerability Notes" and follows up on the IPA/JPCERT Vulnerability reports, US-CERT Alerts, US-CERT Vulnerability Notes and NISCC Advisories.

## Slide 6: Other Scoring Methods
Common Vulnerability Scoring System (CVSS):

## Slide 7: Other Scoring Methods (CONT’D)
National Vulnerability Database Version 2.2 (NVD):

## Slide 8: Other Scoring Methods (CONT’D)

## Slide 9: Other Scoring Methods (CONT’D)
JVNRSS: CVSS Version 2.0 (JVN):

## Slide 10: Scope of Risk Assessment
Evaluation and assessment, to identify assets and evaluate their properties and characteristics.
Risk assessment, to discover threats that pose risk to assets which becomes vulnerabilities.
Risk mitigation, to address risk by transferring, eliminating or accepting it.

## Slide 11: Purpose of Risk Assessment
The purpose of this chapter is to provide a method for performing
vulnerability and threat analysis towards risk assessment and
answer the following questions.
What needs to be protected?
Who/What are the threats and vulnerabilities?
What are the implications if they were damaged or lost?
What is the value to the organization?
What can be done to minimize exposure to the loss or damage?

## Slide 12: Basic Terminology
Risk: IT security risk is the potential harm to a process or related information resulting from some purposeful or accidental event that negatively impacts the process or the related information.
Example:
Buffer Overflow allows remote attackers to gain root access using a long
PASS command
Denial of Service allows a remote attacker to cause a crash.

## Slide 13: Basic Terminology (Cont’d)
Vulnerability:
It is defined as a “weakness of an asset or group of assets that can be exploited by one or more threats”.
Examples of vulnerability exploits:
1. An attacker finds and uses an overflow weakness to install malware to export sensitive data.
2. An attacker convinces a user to open an email message with attached malware.

## Slide 14: Basic Terminology (Cont’d)
Threat:
It is defined as “Any circumstance or event with the potential to adversely impact an asset through unauthorized access, destruction, disclosure, modification of data, and/or denial of service”.
Examples of threat :
1.Bugs in hardware and power failures.
2.Non-malicious and malicious threats, such as disgruntled employees and hackers.

## Slide 15: Basic Terminology (Cont’d)
Counter Measure(CM):
It is an action, device, procedure, or technique that reduces a threat, a vulnerability, or an attack by eliminating or preventing it, by minimizing the harm it can cause, or by discovering and reporting it so that corrective action can be taken.
Lack of Counter Measure(LCM): The complement of CM gives LCM. i.e. LCM = 1- CM

## Slide 16: Security Meter (Sm) Model Design
Data for malicious attacks that have been prevented or not prevented must be collected. Figure below shows that the constants are the utility cost (asset) and criticality constant (between 0 and 1), whereas the probabilistic inputs are vulnerability, threat, and lack of countermeasure (LCM=1-CM) of all risks between 0 and 1.

## Slide 17: Input/Output Table for Risk Assessment
An input/output table will be created in database to store values:
Vulnerability
Threat
Count of Vulnerability
Count of Threat
Probability of Vulnerability
Probability of Threat
Lack of Counter Measure(LCM)
Counter Measure(CM)
Optimized Counter Measure
Residual Risk
Optimized Residual Risk

## Slide 18: Security Meter (Sm) Model Design
The residual risk (RR: as in Figure below) and expected cost of loss (ECL) are the outputs obtained using equations shown in next slide. The black box in Figure in above slide leads to the probabilistic tree diagram of Figure below to do the calculations.

## Slide 19: Security Meter (Sm) Model Design (cont’d)
The following equation computes the RRs for each activity in the above Figure for each leg:
Covering all legs in a tree diagram, RR’s (0<RR<1) summed total to Total Residual Risk, TRR (0<TRR<1) as shown in Figure above.

## Slide 20: Security Meter (Sm) Model Design (cont’d)
The proposed Security Meter’s(SM) mathematical accuracy is verified by a Monte Carlo statistical simulation study.
Five thousand runs, one of which is shown in Figure beside resulting in 24.85% total residual risk, are conducted by generating random variables from each vulnerability, threat, or countermeasure.

## Slide 21: Addition and Multiplication Laws of Probability
Tree Diagram: Given that in a simple sample scenario, there are two or three or more of each choice, the following probabilistic frame holds.
Addition Law:
Note: Sum of Vi=1 and sum of Tij=1 for each i, and Sum of LCM+CM=1 for each j, within a tree diagram structure.

## Slide 22: Simplified Computer Security Risk Tree Diagram with the Security-Meter Design to Illustrate the Multiplication Law

## Slide 23: A Real World Example to Implement the Security-Meter Design using Survey Results
In a recent field study by L. W. from Nova Southeastern Univ. to implement the security model, CSI/FBI, Deloitte and Pricewaterhouse survey results were evaluated regarding the security concerns at the University of Virgina School of Continuing and Professional Studies Northern Virginia Regional Center (from now on, Center). The Center’s Senior Network Administrator estimated the servers in May 2006 to be worth $8,000.00. With a general risk assessment in mind and the quantitative security meter method selected, the next step was to determine the scope of the risk assessment project.
To be continued on the next pages 24 to 37.

## Slide 24
CSI / FBI Survey Countermeasure | % Of Respondents Reporting Them
Firewalls | 97 (=CM13)
Anti-Virus Software | 96 (=CM23)
Security Audits | 80 (=CM14)
Intrusion Detection Systems (IDS) | 72 (=CM31)
Security Awareness Policy Training | 70 (=CM11)
Server-Based Access Control Lists (ACL) | 70 (=CM32)
Encryption For Data In Transit | 68 N/A, redundant, not used in the final table
Reusable Account/Login Passwords | 52 N/A, redundant, not used in the final table
Encrypted Files | 46 (=CM33)
Smart Cards/ One-Time Password Tokens | 42 (=CM12)
Public Key Infrastructure | 35 (=CM21)
Intrusion Prevention Systems | 35 (=CM22)
Biometrics | 15 N/A, redundant, not used in the final table
Table 1: Security Meter Probability Source Data for Countermeasure actions utilized

## Slide 25
CSI / FBI Survey Threats and CIO / Pricewaterhouse Survey Threats | % Of Respondents Reporting Them
Virus | 66 (=T23)
Malicious Code | 59 (=T32)
Insider Abuse of Net Access | 48 (=T11)
Laptop/Mobile Theft | 48 N/A, redundant, not used in the final table
Unauthorized Access to Information | 32 (=T31)
Denial of Service (DOS) | 32 (=T13)
Abuse of Wireless Network and Web Site Defacement | 22 (=T21)
System Penetration | 16 (=T12)
Theft of Proprietary Information | 9 (=T33)
Misuse of Public Web Application | 5 N/A, redundant, not used in the final table
Financial or Telecom Fraud | 4 (=T14)
Sabotage | 2 (=T22)
Table 2: Security Meter Probability Source Data for Threats utilized

## Slide 26
Deloitte Survey Vulnerabilities | % Of Respondents Reporting Them
Internal Security Breach only | 35 (=V1)
External Security Breach only | 26 (=V2)
Both Internal and External Security Breach | 39 (=V1 and V2)
Table 3: Security Meter Probability Source Data for Vulnerabilities utilized in Table 19.

## Slide 27
Criticality Definition | Value Rating Factor
Asset’s Loss has negligible impact on Center’s mission | 0.0
Asset’s Loss has minor impact on Center’s mission | 0.2
Asset’s Loss has moderate impact on Center’s mission | 0.4 (selected in this example)
Asset’s Loss has significant impact on Center’s mission | 0.6
Asset is mission-critical to the Center. Loss would have serious impact on Center’s Mission. | 0.8
Asset is mission-essential to the Center. Center could not absolutely carry out mission without it. | 1.0
Table 4: Asset Criticality Rating for the Security Meter Design for an Asset of $8,000.00.

## Slide 28
Vulnerability | Threat | Countermeasure
V1 = 0.35 (Internal Security Breach Only ) | T11 = 0.48 (Internal Abuse of Network Access) | CM11 = 0.70 (Security Awareness Policy Training) LCM11=0.30 by Subtraction
 | T12 = 0.16 (System Penetration) | CM12 = 0.42 (Smart Cards/Other One-Time Password Tokens) LCM12 = 0.58 by Subtraction
 | T13 = 0.32 (Denial of Service | CM13 = 0.97 (Firewalls) LCM13 = 0.03 by Subtraction
 | T14 = 0.04 (Financial / Telecom Fraud) | CM14 = 0.80 (Security Audits) LCM14 = 0.20 by Subtraction
V2 = 0.26 (External Security Breach Only) | T21 = 0.32 (Denial of Service) | CM21 = 0.35 (Public Key Infrastructure) LCM21 = 0.65 by Subtraction
 | T22 = 0.02 (Sabotage) | CM22 = 0.35 (Intrusion Prevention Systems) LCM21 = 0.65 by Subtraction
 | T23 = 0.66 (Virus) | CM23 = 0.96 (Anti -Virus Software) LCM23 = 0.04 by Subtraction
Table 5. Security Meter Probability Table for a Production server at The Center

## Slide 29
V3 = 0.39 (Both Internal and External Security Breaches Only) | T31 = 0.32 (Unauthorized Access to Information) | CM31 = 0.72 (Intrusion Detection Systems) LCM31 = 0.28 by Subtraction
 | T32 = 0.59 (Malicious Code) | CM32 = 0.70 (Server Based Access Control) LCM32 = 0.30 by Subtraction
 | T33 = 0.09 (Theft of Proprietary Information) | CM33 = 0.46 (Encrypted Files) LCM33 = 0.54 by Subtraction
Table 5 continued: Security Meter Probability Table for a Production server at The Center

## Slide 30
Table 6. Risk Management Spreadsheet prepared from Tables 1 and 5 to break even at $513 (difference due to round-off errors) for 90.52% countermeasure (CM) improvement with final RR = 10%.

## Slide 31: Table 7: Game Theoretic Cost-Optimal Risk Management by Neumann and Nash

## Slide 32: Table 8: Diagonal Loss Matrix (Cols 1-3,5 of Neumann; Col 12 of Nash)

## Slide 33: Mathematical Observations
Interesting (unusual) tableau, because all elements are diagonals. And also all elements of the matrix are both max and min due to being singletons. Then we simply choose a minimum column-wise and maximum row-wise, which are not equal.
CONCLUSION: The game-theory application software stabilized this lack of equilibrium into a desired two-player zero-sum game. This provides a list of countermeasure probabilities, CM11 with prob. 1.0, CM12 with 0.42…CM33 with 0.46 etc.. This is the optimal mixed strategy for Company B (defense) to minimize its expected loss while Company A (offense) maximizes its gain. Now the game plan is at equilibrium. Defense and Offense cannot change the game by altering CMij.

## Slide 35: Nonlinear Minimization of the Portfolio Variance (= Average of the sum of squares of the deviations from the mean value under each scenario ) s.t. a constraint on the expected return of the portfolio.
MIN = 1/10*(R1-Rb)^2 + 1/10*(R2 -Rb)^2 + 1/10*(R3 -Rb)^2 + 1/10*(R4 - Rb)^2 + 1/10*(R5-Rb)^2 + (R6 -Rb)^2 + 1/10*(R7 -Rb)^2 + 1/10*(R8 - Rb)^2 + 1/10*(R9-Rb)^2 + 1/10*(R10 - Rb)^2;
1*X1 < 1; 1*X2 < 1; 1*X3 < 1; 1*X4 < 1; 1*X5 < 1; 1*X6 < 1; 1*X7 < 1; 1*X8 < 1; 1*X9 < 1; 1*X10 < 1;
1*X1 >0.7;
1*X2 > 0.42;
1*X3 > 0.97;
1*X4 > 0.8;
1*X5 > 0.35;
1*X6 > 0.35;
1*X7 > 0.96;
1*X8 > 0.72;
1*X9 > 0.7;
1*X10 > 0.46;
0.168*X1 = R1;
0.056*X2 = R2;
0.112*X3 = R3;
0.014*X4 = R4;
0.057*X5 = R5;
0.0052*X6 = R6;
0.1976*X7 = R7;
0.1248*X8 = R8;
0.2301*X9 = R9;
0.0351*X10 = R10;
1/10*(R1 + R2 + R3 + R4 +R5 + R6 + R7 + R8 + R9 + R10) = Rb;
Rb > 0.09;

## Slide 36: Portfolio Approach (Markowitz Nonlinear Optimization Solution by LINGO Software):
Porfolio Approach (MArkowitz Nonlinear Optimization Solution):
Rows= 33 Vars= 21 No. integer vars= 0 Nonlinear rows= 1 Nonlinear vars= 11
Objective value: 0.1026704E-01
Variable Value
R1 0.1451340
RB 0.9000000E-01
R2 0.5600000E-01
R3 0.1120000
R4 0.1400000E-01
R5 0.5700000E-01
R6 0.5200000E-02
R7 0.1896960
R8 0.1248000
R9 0.1610700
R10 0.3510000E-01
X1 0.8638929
X2 1.000000
X3 1.000000
X4 1.000000
X5 1.000000
X6 1.000000
X7 0.9600000
X8 1.000000
X9 0.7000000
X10 1.000000

## Slide 37: Nonlinear Portfolio Risk Table

## Slide 38: Conclusion: COCOA (Cost Optimal Countermeasure Allocation)
Game Theory Approach yields better economical results than the Portfolio (Markowitz) for the same SEC-METER scenario, 90.52% vs. 309%, and if the same cost factor is used as in the earlier COCOA approach, then 309-90.5= 218.5% times $5.67 would save $1239.

## Slide 39: Java Coded Game-Theoretic Optimal Solution

## Slide 40: MONTE CARLO SIMULATION AND MATH-STATISTICAL TRIPLE PRODUCT RULE
The Triple Product Rule of Uniforms:
For determining the distribution of the product of three Ui (ai , bi), where W= xyz, the pdf of V can be found by applying the well-known Rohatgi result for the case of two random variables.
Let’s take the ‘two random variables’ (rv) case before the challenge of the 3 rv case. Assume that the continuous rv X is distributed with f(x) = U (a, b), and rv Y is distributed with g(y) = U(c, d).
The pdf of V=XY is therefore given using the transformation of variables, where the proofs are presented in references by the respective authors, Leemis, Glenn, and Drew, 2004.

## Slide 41: MONTE CARLO SIMULATION AND MATH-STATISTICAL TRIPLE PRODUCT RULE (cont’d)
The Triple Product Rule of Uniforms:

## Slide 42: MONTE CARLO SIMULATION AND MATH-STATISTICAL TRIPLE PRODUCT RULE (cont’d)
The Triple Product Rule of Uniforms:
Take, for example, the rv X with U (a=1, b=2) and Y with U(c=3, d=4). To determine the distribution of V=XY, one can use the MAPLE code, or simply using the previous h (v) derivation, where ac< bd.

## Slide 43: MONTE CARLO SIMULATION AND MATH-STATISTICAL TRIPLE PRODUCT RULE (cont’d)
The Triple Product Rule of Uniforms:
The plot of the pdf of the rv V=XYZ, the triple product of the continuous uniforms and additionally the mean and variance of V is as follows using MAPLE software program.
> PlotDist (V):

## Slide 44: MONTE CARLO SIMULATION AND MATH-STATISTICAL TRIPLE PRODUCT RULE (cont’d)
Data Analysis on the Total Residual Risk of the Security Meter Design:
An example inspired from the Security meter application of a home PC will be studied below, See the Table below:

## Slide 45: MONTE CARLO SIMULATION AND MATH-STATISTICAL TRIPLE PRODUCT RULE (cont’d)
Data Analysis on the Total Residual Risk of the Security Meter Design:
When we apply a Monte Carlo simulation to the PC example in the Table above following n = 1,000,000 simulation runs, we also get almost an identical expected value, TRR (M) = 0.239385, which is very satisfactorily compared to M = 0.239375 (exact) in the MAPLE solutions.

## Slide 46: MONTE CARLO SIMULATION AND MATH-STATISTICAL TRIPLE PRODUCT RULE (cont’d)
Data Analysis on the Total Residual Risk of the Security Meter Design:
Monte Carlo Simulations for the PC example as in the TABLE above.

## Slide 47: Modifying the SM Quantitative Model for Categorical, Hybrid and Non disjoint Data
Sometimes we do not possess purely quantitative values for each of the attributes in the decision tree diagram, and all that are available are qualitative adjectives such as H (high; often), M (medium; occasional), or L (low; occasional), or even W (rare, unlikely) or more such as Z (very rare; very unlikely) etc. which may extend to all letters of the alphabet as so formulated if necessary.
We can then for instance use the probabilities of H, M, and L, i.e., P(H), P(M) and P(L), as long as the addition rule of unity holds for disjoint events (the first three laws of probability).
Such outcomes of vulnerability (first branch of the tree diagram) or threat (second branch) may include H + L = 1, or M + L + L = 1 or L + L + L + L = 1, where H = 0.75, M = 0.5, and L = 0.25 hold, where we have dropped the probability symbol P, for simplicity.

## Slide 48: Modifying the SM Quantitative Model for Categorical, Hybrid and Non disjoint Data (cont’d)
The Table below illustrates a simple design. The following are vulnerabilities, threats and countermeasures for such a design.

## Slide 49: Modifying the SM Quantitative Model for Categorical, Hybrid and Non disjoint Data (cont’d)
Qualitative Analysis:

## Slide 50: Modifying the SM Quantitative Model for Categorical, Hybrid and Non disjoint Data (cont’d)
Hybrid Analysis:

## Slide 51: Modifying the SM Quantitative Model for Categorical, Hybrid and Non disjoint Data (cont’d)
An Example for 3 x 3x 2 SM Designs to accommodate hybrid input data.

## Slide 52: Modifying the SM Quantitative Model for Categorical, Hybrid and Non disjoint Data (cont’d)
Let (n=2) for vulnerabilities in Figure below:
P (v1) = 0.65 P (v2) = 0.55
Then, P (v1 U v2) = P (v1) + P (v2) - P (v1 ∩ v2)
P (v1 ∩ v2) = 0.2 (v1 and v2 are non disjoint)

## Slide 53: Modifying the SM Quantitative Model for Categorical, Hybrid and Non disjoint Data (cont’d)
Let (n=2) for vulnerabilities in Figure below:
P (v1) = 0.65 P (v2) = 0.55
Then, P (v1 U v2) = P (v1) + P (v2) - P (v1 ∩ v2)
P (v1 ∩ v2) = 0.2 (v1 and v2 are non disjoint)
Since, P (v1). P (v2) ≠ P (v1 ∩ v2),
v1 and v2 are dependent.
P (v1 ∩ v2c) = 0.45
P (v2 ∩ v1c) = 0.35
P (v2 ∩ v1) = 0.2
P (v2c ∩ v1c) = 0

## Slide 54: Modifying the SM Quantitative Model for Categorical, Hybrid and Non disjoint Data (cont’d)
Let (n=2) for threats in Figure beside:
Let:
P (t1) = 0.8
P (t2) = 0.7
Then,
P (t1 U t2) = P (t1) + P (t2) - P (t1 ∩ t2)
P (t1 ∩ t2) = 0.5 (t1 and t2 are non disjoint)
P (t1 ∩ t2c) = 0.3; P (t2 ∩ t1c) = 0.2;
P (t1c ∩ t2c) = 0; P (t1) P (t2) ≠ P (t1 ∩ t2),
and t1 and t2 are dépendent.

## Slide 55: Modifying the SM Quantitative Model for Categorical, Hybrid and Non disjoint Data (cont’d)
Let:
P (v1) = 0.55
P (v2) = 0.45 P (v3) = 0.45
P (v1 ∩ v2) = 0.15
P (v1 ∩ v3) = 0.25 P (v3 ∩ v2) = 0.10;
P (v1 ∩ v2 ∩ v3) = 0.05
P (v1 ∩ v2 ∩ v3c ) = 0.1
P (v1 ∩ v3 ∩ v2c) = 0.2
P (v3 ∩ v2 ∩ v1c) = 0.05
P (v1 ∩ v2c ∩ v3c ) = 0.2
P (v2 ∩ v1c ∩ v3c) = 0.25
P (v3 ∩ v2c ∩ v1c) = 0.15
P (v1c ∩ v2c ∩ v3c) = 0

## Slide 56: Modifying the SM Quantitative Model for Categorical, Hybrid and Non disjoint Data (cont’d)
General Venn diagram for n=3:

## Slide 57: Modifying the SM Quantitative Model for Categorical, Hybrid and Non disjoint Data (cont’d)
Let (n=3) for threats in Figure beside.
Let:
P (t1) = 0.36
P (t2) = 0.46 P (t3) = 0.55
P (t1 ∩ t2 ∩ t3c) = 0.05
P (t1 ∩ t3 ∩ t2c) = 0.1 0.2
P (t3 ∩ t2 ∩ t1c) = 0.2
P (t1 ∩ t2c ∩ t3c) = 0.2 P (t2 ∩ t1c ∩ t3c) = 0.2
P (t3 ∩ t2c ∩ t1c) = 0.24
P (t1 ∩ t2 ∩ t3) = 0.01
P (t1c ∩ t2c ∩ t3c) = 0

## Slide 58: Modifying the SM Quantitative Model for Categorical, Hybrid and Non disjoint Data (cont’d)
The SM tree diagram to represent for a n=2 non disjoint scenario.

## Slide 59: Modifying the SM Quantitative Model for Categorical, Hybrid and Non disjoint Data (cont’d)
The Risk Quantifier Software for a n=2 non disjoint converted into a disjoint scenario for the following new example:
Input: P(v1) = 0.6, P(v2) = 0.5P(v1 ∩ v2) = 0.2; P(v1’ ∩ v2’) = 0.0.
Output: v1∩ v2’=0.6 – 0.2 = 0.4; v2 ∩ v1’=0.5–0.2=0.3; v1 ∩ v2=0.2; v1’∩v2’=1–(0.4+ 0.3+0.2) = 0.1.

## Slide 60: Modifying the SM Quantitative Model for Categorical, Hybrid and Non disjoint Data (cont’d)
The SM tree diagram to represent for a n=3 non disjoint scenario.

## Slide 61: Maintenance Priority Determination for 3 X 3 X 2 SECURITY METER
Software maintenance, as a general process of making changes to improve a system after its installation can involve,
1) the adaptation of software to a new operating environment,
2) the repair of software faults, ranging from coding errors which are the cheapest to fix, to design errors which are more expensive, and finally to requirement errors, which are the most expensive and
3) adding or modifying the system’s functionality due to internal and external factors such as changing laws and changing markets or business structures.
are shown in the slide below.

## Slide 62
Security Meter calculations for the previous tree diagram

## Slide 63: Maintenance Priority Determination for 3 X 3 X 2 SECURITY METER (cont’d)
A priori existence and a posteriori defectiveness probabilities of vulnerabilities.

## Slide 64: Maintenance Priority Determination for 3 X 3 X 2 SECURITY METER (cont’d)
Risk Quantifier for 3 x 3 x 2 SM Design with Maintenance
(! Signifies: Needs Overhaul).

## Slide 65: Maintenance Priority Determination for 3 X 3 X 2 SECURITY METER (cont’d)
Security Meter calculations for a 3 x 3 x 2 SM Design with data as in the Risk Quantifier.

## Slide 66: Privacy Meter (PM): How to Quantify the RISK OF Breach of Privacy
Tree Diagram for the 3 x 3 x 2 SM Design to accommodate the apriori and a posteriori risks.

## Slide 67: Privacy Meter (PM): How to Quantify the RISK OF Breach of Privacy (cont’d)
Tree Diagram for the 3 x 3 x 2 SM Design to accommodate the a priori and
a posteriori risks.

## Slide 68: Privacy Meter (PM): How to Quantify the RISK OF Breach of Privacy (cont’d)
Methodology:
In repairable systems, repair actions take place in response to the observed failures and the system is returned to the field as good as new. A stochastic model could be experiencing a constant rate of failure (CFR), an increasing (IFR) or a decreasing rate (DFR). In a homogeneous Poisson Process (HPP), or Poisson, there are no trends and the rate is CFR.
Further, there may occur more than a single breach at an interval for the NHPP where the size of events at each interval is represented by a compound Poisson process. That is, if the governing process is NHPP, and the size of clusters is geometric with forgetfulness property, the compound Poisson is Poisson ^ Geometric. If otherwise, the outcomes within a cluster are correlated assuming a compounding probability mass function of logarithmic series, then the CP is defined to be Poisson^ logarithmic series or a Negative Binomial.

## Slide 69: Privacy Meter (PM): How to Quantify the RISK OF Breach of Privacy (cont’d)
Privacy Risk-o-Meter Assessment and Management Examples:
Probability Tables (before the Countermeasures are taken).

## Slide 70: Privacy Meter (PM): How to Quantify the RISK OF Breach of Privacy (cont’d)
Privacy Risk-o-Meter Assessment and Management Examples:
Probability Table (after the Countermeasures are applied).

## Slide 71: Privacy Meter (PM): How to Quantify the RISK OF Breach of Privacy (cont’d)
Privacy Risk-o-Meter Assessment and Management Examples:
After the countermeasures are taken, P(X ≥ 260) = 0.0041= 0.4%. The risk defined by the bank has been mitigated by a margin of 34.56% to a low of 0.4% from a high of 34.96%.
The risk has been mitigated by a solid 34.56%, amounting to a benefit of 34.56 x $100,000 = $ 3,456,000, if each 1% slot on the average signifies a benefit of $100,000 in avoiding identity thefts. Overall, the bank is profiting almost $3.5 million from this transaction, i.e., by not losing from future identity thefts and privacy breaches, since the $3.5 million benefit advantages clearly exceed the $500,000 cost for improvement.
Profit = Benefit−Cost = $ 100(.3496 - .004074) x100, 000 (benefit) −$500,000 (cost) =$2,955,716 .

## Slide 72: POLISH DECODING (DECOMPRESSION) ALGORITHM
The following is the approach taken to recreate the RBD from a given Polish notation:
1. Accept the Polish notation from the user. The Polish notation consists of nodes (numbers) and operators (* or +).
2. Parse the Polish notation to identify the nodes and operations.
3. Identify the node pairs that connect. Use the existing Java components and the node pairs that are identified to draw the RBD.

## Slide 73: POLISH DECODING (DECOMPRESSION) ALGORITHM (cont’d)
A stack algorithm was employed to accomplish the above.
1. Push into the stack until an operator is encountered.
2. If the operator is a * (nodes in series):
a. Pop the top two elements (nodes) of the stack.
b. Form a node pair.
c. Concatenate the nodes and node pairs.
d. Push the concatenated string onto the top of the stack.
3. If the operator is a + (nodes in parallel)
a. Pop the top two elements (nodes) of the stack.
b. Concatenate the operator between the two nodes.
c. Push the concatenated string on to the top of the stack.
4. Continue performing the foregoing steps until the end of the Polish notation.

## Slide 74: POLISH DECODING (DECOMPRESSION) ALGORITHM (cont’d)
If the topology is of prime interest, the decoding algorithm is of value to transport very complex networks safely and discreetly with extremely complicated Polish notations hard to decipher such as shown in below.

## Slide 75: Discussions and Conclusion
The incentives for evaluating security risks are so compelling and indispensable that we should and could, rather than might, be making meaningful estimates [G. Cybenko, Why Johnny Can’t Evaluate Risk, IEEE Security and Privacy, 4(5), 2006]. The difficulty in data collection and parameter estimation pose a challenge to practitioners in the testing field.
The author has employed the concept of a simple relative frequency approach, otherwise known as a counting technique [M. Sahinoglu, Security Meter: A Practical Decision Tree Model to Quantify Risk, IEEE Security and Privacy, 3(2), 2005]
The overlap method with its extreme speed and additional advantages, such as multistate treatment of components is also studied in this chapter through algorithms for hand calculations as the subject matter of a new RBD trend. The set of algorithms presented for students and readers toward earlier unsolvable complex networks, now feasible by hand calculations is a powerful alternative to commercial software only.

## Slide 76: THANK YOU!