## Slide 1
Chapter 6
Modeling AND SIMULATION in cyber-risk
Cyber-Risk Informatics: Engineering Evaluation with Data Science

## Slide 2: Learning Objectives
Describe the concept of simulation with its static and dynamic components, and its relevance to cyber-risk informatics and risk engineering.
Explore the innovative and popular theme of engineering modeling and simulation, predominantly in the manufacturing industry and cybersecurity world, citing severe challenges, advantages and time- and budget saving solutions and its future.
Study a cross section of Engineering Modeling and Simulation practices illustrating a window of numerical examples with relevant and useful statistical modeling.

## Slide 3: Abstract
The power of simulation is not an exaggeration but an understatement. This refers not only to research findings in verifying a certain piece of theory, such as that of the recently discovered Higgs Boson, but in testing new products to innovate new discoveries so as to make our universe a more peaceful place by modeling and simulating the future projects and taking precautions before disasters occur. Computer Modeling and Simulation (M&S), as programs or networks of computers mimicking the execution of an abstract model of many natural systems from physical and life sciences to social and managerial sciences, and primarily engineering, have become an integral part of digital experimentation. M&S proves useful to estimate the performance of complex engineering systems when too prohibitive for analytical solutions. A simulation is defined as the reproduction of an event with the use of scientific models. A model is a physical, mathematical, or other logical representation of a system, process or phenomenon. Time-independent static Monte Carlo (MC) or conversely dynamic Discrete Event Simulation (DES) to manage events in real time for engineering applications will be reviewed.
Keywords: Discrete Event/Monte Carlo, Modeling, Production, Cyber-risk informatics, Bayesian, Multistate, Multichannel Queuing Simulation

## Slide 4: KEY CONCEPTS
Computer Modeling and Simulation (M&S), as programs or networks of computers mimicking the execution of an abstract model of many natural systems from physical and life sciences to social and managerial sciences, and primarily engineering, have become an integral part of digital experimentation. M&S proves useful to estimate the performance of complex engineering systems when too prohibitive for analytical solutions.
A simulation is defined as the reproduction of an event with the use of scientific models. A model is a physical, mathematical, or other logical representation of a system, process or phenomenon.
Time-independent static Monte Carlo (MC) or conversely dynamic Discrete Event Simulation (DES) to manage events in real time for engineering applications will be reviewed.

## Slide 5: INTRODUCTION AND a Brief History to Simulation
The favorable outcomes since the advent of digital computers and software revolution could not have been achieved, especially without the multiple benefits of statistical simulation, which underlies the widespread use of modeling and simulation in engineering and sciences, stretching from A (Anthropology) to Z (Zoology).
Modern computer simulation developed in parallel with the rapid-growth of computer use during the development of the Manhattan Project in WWII to nondestructively model and simulate the nuclear detonation before it was destructively dropped on Hiroshima and Nagasaki in Japan in 1945.
Therefore, the history of simulation is interesting and intriguing.

## Slide 6: INTRODUCTION AND a Brief History to Simulation (cont’d)
Computer simulation has been widely used in engineering systems to validate the effectiveness of tentative decisions regarding a new plan or schedule, or its outcomes, without actually experiencing the actual conditions, which could in actuality cost more resources or partial to full destruction such as in the simulation of the nuclear bomb.
Taxonomy-wise, simulated computer models may be stochastic or deterministic, and dynamic or static, and discrete or continuous.
The IEEE June 2012 Spectrum issue, emphasized that the Modeling and Simulation effect is a creative and time-saving topic of interest ranging from automotive engineering of hybrid vehicles to finding solutions to treating nuclear waste, and upgrading the nuts and bolts of the Electrical Power (Smart) Grid and moreover, supercomputing research.

## Slide 7: GENERIC THEORY - CASE STUDIES ON GOODNESS OF FIT FOR UNIFORM NUMBERS
A formal scientific theory of simulation, to verify a validated model so as to mimic a physical or a social system, does not exist in terms of conventional math-statistical theorems and their subsequent proofs.
The fundamental process of verifying sequences of uniform deviates from an associated generator where Ho: Uniform Random Sequence is (quasi) random vs. Ha: Sequence is not random, is an accepted technique.
The results show that by law of large numbers for only n≥N≈50,000; E(Ө)→0.5 with probability 1, for Ө ~ Uniform(0,1) from the uniform number generator imbedded in the Java code, “Ho: Random Sequence” is not rejected. Therefore n=50,000 runs is a new standard for attaining quasi-randomness; not 5,000 anymore as practiced in ‘80s.

## Slide 8: Why Crucial to Manufacturing and Cyber Defense Issues
The power of simulation is prevalent as a related audio-visual favorably explains certain topics related to Production and Manufacturing Engineering. In “Modeling and Simulation in Manufacturing and Defense Systems Acquisition”, the Board on Manufacturing and Engineering Design (BMED) emphasized the importance of modeling and simulation in not only making the right decisions but also incurring fewer expenses.
There are few simulation studies in cybersecurity-and-defense-related theoretical and applied research. In their 2007 article as titled, “Cyber Attack Modeling and Simulation for Network Security Analysis”, the authors Kuhl et al. discuss a simulation modeling approach to represent computer networks and intrusion detection systems (IDS) to efficiently simulate cyber-attack scenarios in order to test and evaluate cyber security systems.

## Slide 9: Why Crucial to Manufacturing and Cyber Defense Issues (cont’d)
Adjacent Figure displays the interaction between the process of building a model by focusing on the interplay between: a) experimental results, b) simulation results and c) theoretical predictions.
The resulting availability of this small Cloud (see Chap 6 in the text): a) 0.307 for Experimental, b) 0.305 for Simulation after 1 million runs, or trials. and b) 0.331 for Markov Theoretical, allowing a negligible error content, which diminishes to less than 3% as the size of the experiment increases In the event of large cyber CLOUDS, the author showed that the experimental approach was infeasible, and theoretical result was not mathematically tractable.

## Slide 10: A Cross Section of Modeling and Simulation Issues in Manufacturing
Simulation use in production is not new. For the sake of a few examples, various authors from twenty-five years ago published articles on simulating FMS (Flexible Manufacturing Systems), machine utilizations and production rates, and modeling of AMS (Automated Manufacturing Systems).
Due to a lack of closed-form solutions in the three-state model including DERATED as opposed to that of the conventional UP and DOWN dichotomous two-state model, a summary of three or multi-state system inferential analysis will be reviewed by using Monte Carlo simulations.
This process will employ the empirical Bayesian principles to estimate the full and derated availability probability distributions. The historical failure and repair data, or operating (full or derated) and non-operating hours, as the input data, will be used along with prior parameters for an empirical Bayesian analysis.

## Slide 11: Modeling and Simulation of Multi-State Production Units and Systems in Manufacturing (cont’d)
Most research articles or books on reliability theory are devoted to traditional binary reliability models allowing for only two possible states for a system and its components: perfect functionality or complete failure.
However, many real-world systems are composed of multi state components which have different performance levels and several failure modes with varying effects on the entire system performance. Such systems are called multi-state systems (MSS).
Examples of MSS are cyber systems where the unit performance is characterized by the data processing speed or server gigabyte capacity and similar to electric power systems, where the generating unit performance is depicted by its generating capacity. In the electric power supply system of generating facilities, each generator can function at different levels of capacity with a given probability.

## Slide 12: Modeling and Simulation of Multi-State Production Units and Systems in Manufacturing (cont’d)
The power of simulation once again flexes its muscle as a favorable exit out of this theoretical impasse. The Monte Carlo technique remains the only available feasible way to solve the proposed three-state problem, whose math-statistical closed-form solution does not actually exist.
The failure and repair rates were taken to be the generalized gamma random deviates where the corresponding gamma shape and scale parameters respectively were not equal. The two-state SL density was shown to default to that of a standard two-parameter beta density function when the shape parameters are identical.
The stochastic method proposed was superior to estimating availability by dividing total uptime by exposure time. Following the Monte Carlo simulations, analytical pdfs of the multiple states will be approximated using their associated moments.

## Slide 14: Two – State Sahinoglu - Libby (SL) Probability Model of REPAIRABLE Units
In using the distribution function technique, the pdf of FOR = q = [λ/(λ+µ)] is obtained first by deriving its cumulative density function (cdf), i.e. GQ(q) = P (Q  q) = P [λ/(λ+µ)]  q).
Then, taking its derivative to obtain gQ(q) per equations is as follows:

## Slide 15: Two – State Sahinoglu - Libby (SL) Probability Model of REPAIRABLE Units (cont’d)
Note that gQ(q) is the pdf of the random variable Q = FOR, where α = a + c, β = b + d , β 1 = 𝛏 + xT , and β 2 = 𝛈 + yT ; and 0  q  1. If L= for SL (α, β, L) or β 1 = β 2, the usual two-parameter beta pdf is obtained.
An alternative original derivation of the same pdf termed under generalized multivariate beta distribution is given by Libby in 1981 and 1982.
The expression in equation mentioned in above slide can also be reformulated in terms of SL (α= a + c, β = b + d, L= ), as follows:

## Slide 16: Two – State Sahinoglu - Libby (SL) Probability Model of REPAIRABLE Units (cont’d)
Note if L = 1, Sahinoglu-Libby pdf reduces to a standard Beta (α, β,) pdf. See Figure below for “r = availability” and “q = unavailability” confidence plots where r =1-q. Densities of SL (or G3B) distributions for a variety of L values.

## Slide 17: Three - State Sahinoglu - Libby Probability Model Of REPAIRABLE UNITS
Let us consider a single derated state rather than multiple ones, which may well exist in practice such as in 50%, 60% or 75% derated capacity.
But now, we have not only full-FOR but also derated-FOR (or DFOR), that will be equal to the total derated operating time over the total exposure time. That is, DFOR = DER time/ (UP time + DER time + DOWN time).
It is also well documented that any calculated FOR or DFOR is not only a constant but also a specific single realization of its random variable.
We shall now review above and beyond a traditional closed-form two-state SL; namely, a three-state SL where the transition rates are gamma distributed.

## Slide 18: Three - State Sahinoglu - Libby Probability Model Of REPAIRABLE UNITS (cont’d)
Let us examine and review the following state space diagram.
Let λ= transition rate from UP (fully operational) to DOWN (forced outage) state;
µ= transition rate from DOWN to UP state;
δ = transition rate from UP to DER (partially forced outage) state;
β = transition rate from DER (partially forced outage) to UP state;
α = transition rate from DER to DOWN state;
γ = transition rate from DOWN to DER state.

## Slide 19: Three - State Sahinoglu - Libby Probability Model Of REPAIRABLE UNITS (cont’d)
Using figure given in above slide, by changing to the Greek variables from the Latin originals (a to f) cited in the same reference;
The time-dependent but steady state probabilities of occupying one of the three states are given as follow from below equations, assuming negative exponential densities for each state’s sojourn time, which will converge to.
Note: P(UP)=1-FOR-DFOR not P(UP)=FOR (PLEASE see ERRATA Sheet)

## Slide 20: Three - State Sahinoglu - Libby Probability Model Of REPAIRABLE UNITS (cont’d)
See Figure below for a sample draft scenario to illustrate transitions of the Figure in the previous slide.

## Slide 21: Three - State Sahinoglu - Libby Probability Model Of REPAIRABLE UNITS (cont’d)
A illustration of feasible transitions from the Figure shown above:
UP-to-DOWN Failure Transition Rate (λ) from x1 to w1, or x2 to w2
DOWN-to-UP Recovery Transition Rate (μ) from y1 to x1, or y2 to z1
UP- to-DER Failure Transition Rate (δ) from z1 to u1, or z2 to s2
DER-to-UP Recovery Transition Rate (β) from u1 to x2, or u2 to z2
DER to-DOWN Failure Transition Rate (α) from s1 to y2, or s2 to y3
DOWN to DER Recovery Transition Rate (γ) from w1 to s1, or w2 to u2

## Slide 22: Statistical Simulation of Three-State REPAIRABLE Units to Estimate the Density of UP-DOWN-DER STATES
Table 1 below displays the input data as tabulated for an example analyzed below:
The cumulative probabilities of states are calculated by Monte Carlo Simulation method using input from Table above as follows in Tables 2-4 in the next slides (UP, DER and DOWN states in 100, 1000 and 10000 simulation runs, respectively).

## Slide 23: Statistical Simulation of Three-State REPAIRABLE Units to Estimate the Density of UP-DOWN-DER STATES (cont’d)
Tables 2, 3, 4: UP, DERATED, DOWN for 100, 1,000 and 10,000 Simulations Runs.

## Slide 24: Statistical Simulation of Three-State REPAIRABLE Units to Estimate the Density of UP-DOWN-DER STATES (cont’d)
Figures below are plotted for each of the three states (UP-DOWN-DER):

## Slide 25: Statistical Simulation of Three-State REPAIRABLE Units to Estimate the Density of UP-DOWN-DER STATES (cont’d)

## Slide 26: Statistical Simulation of Three-State REPAIRABLE Units to Estimate the Density of UP-DOWN-DER STATES (cont’d)

## Slide 27: Statistical Simulation of Three-State REPAIRABLE Units to Estimate the Density of UP-DOWN-DER STATES (cont’d)
The input data in Table 1, and simulation results in Tables 2-4 and Figures in the above slides display the cumulative reliability plots of the three states for UP (r), DER (d) and DOWN (q) as shown in the below figure.

## Slide 28: Statistical Simulation of Three-State REPAIRABLE Units to Estimate the Density of UP-DOWN-DER STATES (cont’d)
Given the input table on the l.h.s. column, the pdfs of the 3 states are plotted for UP (r), DER (d), and DOWN (q) with a 90% confidence level showing mode (m), mean (E) with upper & lower confidence as centrality measures for n =100,000 simulation runs as shown below.

## Slide 31: Statistical Simulation of Three-State REPAIRABLE Units to Estimate the Density of UP-DOWN-DER STATES (cont’d)
The Figure below shows relationships between popular distributions for statistical simulations. Using pedagogues from Chapter 1, we refer to P44 (for Pedagogue) to generate random deviates from the Sahinoglu-Libby pdf as follows:

## Slide 32: Statistical Simulation of Three-State REPAIRABLE Units to Estimate the Density of UP-DOWN-DER STATES (cont’d)
Given the following simplest series system of two identical components in Figure below, whose default operational probability for each is P (UP) = 0.9 and hence P (System) = 0.92 = 0.81.
We now force these units have their unavailability rv distributed with SL, where gQ(q) is formulated as follows:

## Slide 33: Example of SL Simulation for Modeling Network of 7 Two-State (UP-DN) REPAIRABLE Units
The analytical result being unknown for a complex system as in the 7-node network depicted in the Figure below, the resulting simulation is 0.785 as in table below.
Final Network: 0.78476 successes out of 100000. Network Reliability = 0.78476 Network Unreliability = 0.21524. Each of the 100 networks simulated 1000 times in 148.36 Seconds.

## Slide 34: A REVIEW OF MODELING AND SIMULATION IN CYBERSECURITY
Modeling and simulation (M&S) is a vital tool that can be leveraged for process improvement, and technology/capability development and evaluation.
It is the process of designing a model of a system and conducting simulated experiments to preview and predict system behavior and evaluate optimal strategies for system operation.
Aggregate Supply and Demand (What-if Analyses), Dynamic Simulations, and Multi-Agent Based Models (ABM), which at a macro level similar to cellular automata, is out of scope for this review.
Some examples of M&S and DES, in the cyber security field will follow.

## Slide 35: Monte-Carlo Value-at-Risk (VaR) Approach by Kim et al. in Cloud Computing
Value-at-Risk (VaR) is a market standard risk measure used by senior management and regulators to quantify the risk level of a firm's holdings.
However, the time-critical nature and dynamic computational workloads of VaR applications make it essential for computing infrastructures to handle bursts in computing and storage resources needs.
This requires on-demand scalability, dynamic provisioning, and the integration of distributed resources.
A VaR calculation will typically start after the end of the trading day, when market data and final positions have been verified. It must be complete, and updated risk numbers must be available, before the start of the next trading day.

## Slide 36: Monte Carlo and Discrete Event Simulations in Security-Meter (SM) Risk Model
Example for Security Meter Risk Modeling and Simulation:
Simplest 2x2x2tree diagram for two threats and for two vulnerabilities in a cyber-risk scenario.

## Slide 38: Monte Carlo and Discrete Event Simulations in Security-Meter (SM) Risk Model (cont’d)
Discrete Event Simulation using Negative Exponential pdf:
Discrete Event Simulation results of the 2 x 2 x 2 security meter sampling design. We observe a result of TRR = 0.0269 ≈ 0.027.

## Slide 39: Monte Carlo and Discrete Event Simulations in Security-Meter (SM) Risk Model (cont’d)
Monte Carlo (Static Time-Independent) Simulation using Poisson pdf:
The Monte Carlo (MC) simulation results of the 2 x 2 x 2 security meter sampling design. Using the same data, as projected, we get the same results in below figure. That is, TRR = 0.0269 ≈ 0.027. Therefore, DES and MC results were identical to four decimals as expected.

## Slide 40: Application of Queuing Theory and Simulation to the Cyber security
Cyber security risk analysis, in the most general sense, can be likened to a queuing scenario where malware events (arrivals) occur unexpectedly and then are counter measured (serviced) with respect to existing service facilities whether single or multichannel.
Simulation, as a computational technique, poses a flexible alternative for studying queuing disciplines and waiting lines.
Multichannel System is used for the purpose of receiving a large volume of requests by computer and/or telephone from customers.
A multichannel system is operated through an extensive open workspace, with work stations that include a computer/telephone for each channel. Too many channels would be a waste of resources; therefore, it is of interest to optimize the number of channels.

## Slide 41: Example 1: SINGLE Recovery-Crew for Application of Queuing Simulation to the Cyber security
Total Cost in Java: TC = (Cw * L) + (Cs * k). L = λW = 0.75 * 4.038984 = 3.029238; Total Cost = (10*3.029238) + (7*1) = $37.29.

## Slide 42: Example 2: DOUBLE Recovery-Crew for Application of Queuing Simulation to the Cyber security

## Slide 43: Example 2: DOUBLE Recovery-Crew for Application of Queuing Simulation to the Cyber security
The improvement is noticeable from 1 to 5 malware-event recovery crew.

## Slide 44: Discussions and Conclusion
The power of simulation is evident from countless number of contemporary research works in addition to industrial and military undertakings to save time and budget.
The objective of applying simulation is to strengthen the advantages of the IT corporate circles and reduce the disadvantages, mainly because of the economic pressure and time constraints in the business world.
Regarding the cyber security science and engineering issues however, implementation of modeling and simulation compared to manufacturing industry is fairly new progressing at an experimental stage.
The multiple cases of positive results render M&S methods among the most useful and practical, as well as affordable algorithms of our time.

## Slide 45: APPENDIX
A.1. Uniform Numbers Testing; Ho: Random vs. Ha: Not Random for 500 runs. Ho is not rejected. See Section 2 for this Table and the following Tables.

## Slide 46: APPENDIX (cont’d)
A.2. Uniform Numbers Testing; Ho: Random vs. Ha: Not Random for 500 runs. Ho is rejected. On the average, one out of 40 cycles of 500 runs = 20,000 simulations will end up rejecting Ho: Random.

## Slide 47: APPENDIX (cont’d)
A.3. Uniform Numbers Testing; Ho: Random vs. Ha: Not Random for 5000 runs. Ho, NOT rejected.

## Slide 48: APPENDIX (cont’d)
A.4. Uniform Numbers Testing; Ho: Random vs. Ha: Not Random for 5000 runs. Ho is rejected. On the average, one out of 10 cycles of 5000 = 50,000 simulations will end up rejecting Ho: Random.

## Slide 49: APPENDIX (cont’d)
A.5. Uniform Numbers Testing;
Ho: Random vs. Ha: Not Random for 10000 runs. Ho is NOT rejected.

## Slide 50: APPENDIX (cont’d)
A.6. Uniform Numbers Testing; Ho: Random vs. Ha: Not Random for 10000 runs. Ho is rejected. On the average, one out of 25 cycles of 10000 = 250,000 simulations will end up rejecting Ho: Random.

## Slide 51: APPENDIX (cont’d)
A.7. Uniform Numbers Testing; Ho: Random vs. Ha: Not Random for 50000 runs. Ho is NOT rejected. After 60 cycles x 50K = 3,000K = 3,000,000 simulations there is still no Reject Ho= Random Sequence. This may signal a cut-off point of no rejection of random sequence from this point on. Safe threshold may be 50K for JAVA coding uniform random number generator.

## Slide 52: APPENDIX (cont’d)
A.8. Uniform Numbers Testing; Ho: Random vs. Ha: Not Random for 100000 runs. Ho is NOT rejected. After 50 cycles x 100K = 5,000K = 5,000,000 simulations, there is still no Reject Ho= Random Sequence. This may signal still no rejection of random sequence from the earlier safe threshold: 50K for a JAVA coding uniform random number generator.

## Slide 53: APPENDIX (cont’d)
A.9. Uniform Numbers Testing; Ho: Random vs. Ha: Not Random for 250000 runs. Ho is not rejected. After 40 cycles x 250K = 10,000K = 10,000,000 simulations there is still no Reject Ho= Random Sequence. Chi-square calculated=7.57 < Chi-square critical value =12.59. Do NOT Reject Ho.

## Slide 54: THANK YOU!